IOP-YANFO-241801515

2.4GHz 18dBi Yagi Antenna

| Electrical Specification |
| --- |
| Frequency range | 2400MHz – 2500MHz |
| Gain | 18 dBi |
| VSWR | 1.5 : 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 15° |
| HPBW / Vertical | 15° |
| Front to back ratio | 25dB |
| Power handing | 10W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Radome color | White |
| Radome material | ABS, UV resistant |
| Weight | 3500g |
| Dimensions | Φ89 × 1000 mm |