IOP-PANFO-581004545

5GHz 10dBi Panel Antenna

| Electrical Specification |
| --- |
| Frequency range | 4900MHz – 5875MHz |
| Gain | 10 dBi |
| VSWR | 2 : 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 45° Max |
| HPBW / Vertical | 45° Max |
| Front to back radio | 15dB |
| Electrical downtilt | 0° |
| Power handing | 2W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Lightning protection | DC ground |
| Radome color | Light gray |
| Radome material | ABS |
| Weight | 107g |
| Dimensions | 114 × 114 × 40 mm |